## Slide 1: Internet Of Things
Lecturer: Reza Arjmandi
Summer 2016
Preface:
Introduction ZeroMQ Open Source Library, Multi Threading, Socket Programming and CLI Development with ncurse library.

## Slide 2
ØMQ
Some open source projects are just too good not to use. ØMQ is one of them. It exists to solve a difficult problem close to our hearts. Using this library, we can have each Raspberry Pi act as a publisher of information for the multiple software consoles acting as subscribers.
To allow multiple consoles to control each Pi sensing station, each sensing station also becomes a subscriber to the console publishers. In effect, we have many-to-many communication in a tidy software API, thanks to ØMQ.
For interesting reading, a nice overview of ØmQ is available here: http://zguide.zeromq.org/page:all.

## Slide 3
Performing Installation ØMQ
The download and installation of ØMQ is almost painless for the Raspberry Pi. Simply allow some time for the compile, which might take a while (step 3):
1. wget http://download.zeromq.org/zeromq-3.2.2.tar.gz
2. ./configure –prefix=/usr/local
3. make
4. make check (optional)
5. make install
If you also want C++ support for ØMQ, you can perform the following additional steps (we’ll use only the C API in this chapter):
1. git clone https://github.com/zeromq/cppzmq.git
2. cd cppzmq
3. sudo cp zmq.hpp /usr/local/include/

## Slide 4
Compiling and Linking
When compiling source code using ØMQ, you need to specify only the directory where the include files were installed:
-I /usr/local/include
For linking, you need the following linker options:
-L/usr/local/lib -lzmq
-Wl,-R/usr/local/lib
The last option tells the executable where to find the ØMQ shared libraries at runtime. Exclude that option when linking on the Mac (or use the provided makefile target mac_console).
$ make
gcc –c –Wall –O0 –g –I/usr/local/include –Wall –O0 –g sensor.c –o sensor.o
gcc sensor.o –o sensor –L/usr/local/lib –lzmq –lncurses –Wl, –R/usr/local/lib
sudo chown root ./sensor
sudo chmod u+s ./sensor
gcc –c –Wall –O0 –g –I/usr/local/include –Wall –O0 –g console.c –o console.o
gcc –console.o –o console –L/usr/local/lib –lzmq –lncurses –Wl, –R/usr/local/lib

## Slide 5
Sensing Station Design
If you need to imagine some kind of use case, imagine that the Raspberry Pi is controlling a jail cell door. The guard who wants to open a door pushes a micro switch button to show SW1=On on the remote consoles (as a request indication). After the monitoring agents check their video monitor, one of them agrees to honor the request by entering 1 on the console (which lights the LED) to open the jail cell door. Pressing 0 closes the latch again (turns off the LED).
The great thing about using ØMQ for networking is that you can do the following:
Run ./sensor with no consoles running
Run any number of ./console (or ./mac_console) programs without the sensor running yet
Run as many consoles as you like
Bring down consoles anytime you like
With a little homework and extra effort, you could monitor multiple sensors as well. That was avoided here, to keep the example as simple as possible.

## Slide 6
Sensing Station Program
The sensing station (Raspberry Pi) is started as follows:
$ ./sensor
The station runs quietly until terminated (it can be shut down from a console). While it runs, it periodically broadcasts (publishes) updates to the consoles with the current status of SW1 and LED.
This is necessary because a console may be offline when the last switch or LED change occurs. Whenever SW1 changes, a broadcast is immediately sent with its new status sw1:%d, where %d is a 1 when the switch is on, and otherwise, a 0.
The LED is changed only at the command of the console program. When the sensor program receives a console message of the form led:%d (over the network), the LED is turned on or off, according to the value of %d (1 or 0).
Once the LED is changed, however, it is rebroadcasted to all consoles, so that the other consoles can see that this has changed. Finally, if the console sends stop: to the sensor, the sensor program shuts down and exits. Pressing ^C in its terminal session will also terminate it.

## Slide 7
Console Program
For the Raspberry Pi or any other Linux distribution, you can build the program simply as follows:
$ make
You’ll need the ncurses development library installed, in addition to ØMQ:
# apt–get install libncurses5–dev
To run the console program, simply launch it with the optional hostname as the first command-line argument (the default is localhost):
$ ./console 192.145.200.14 # Raspberry Pi by IP no.

## Slide 8
Console Program
Following Figure shows the appearance of the console when it first starts up. The ??? show that the console does not yet know the status of the switch or LED. Beside the command-line input, it also shows Online?, indicating that it does not yet know whether the sensor is online. As soon as one message is received, that changes to ONLINE.

## Slide 9
Console Commands
The console commands are all single-character commands and are displayed on the screen.
Typing 0 turns off the LED on the sensor, and typing 1 turns it on. Typing q or Q quits the console. Typing x or X terminates the sensor program. (It would not be good to have this option on a real jail cell control.)
The sensor.c main program gets everything started, by opening the GPIO files (input and output), opening the ØMQ sockets, and creating two threads. The main thread is contained within the main program, within the for loop starting at line 298. The loop simply pulls console commands from the ØMQ socket console at line 299 and then acts upon them.

## Slide 10
Sensor Source Code
There are only two supported console commands:
led:%d: Change LED status
stop:: Shut down the ./sensor program
Line 286 of the main program creates the SW1_monitor_thread. This thread is located in lines 211 to 223. It uses the poll(2) system call in the routine gpio_poll(), to determine when the switch setting changes.
Program execution blocks at line 216, until the switch changes state. Then the status of the switch is captured in rc and relayed to all interested consoles by calling the routine publish_SW1().
The remaining thread is launched in the main program from line 289. It runs in lines 228 through 237. It is a very small loop, which simply updates the consoles every 3 seconds, with the current status of the LED and SW1.
This is necessary so that consoles that are restarted can eventually know the current state of these items.

## Slide 11
Sensor Source Code
The mutex_lock() and mutex_unlock() routines are designed to guard against two threads using the same ØMQ resources at the same time.
Doing so would cause program aborts. The ØMQ library supports a routine named zmq_poll() , which would have simplified things if it could have been used.
Unfortunately, it supports only ZMQ_POLLIN for input. Our switch change driver requires the use of poll(2)'s POLLPRI event, so zmq_poll() will not support us there.

## Slide 12
Sensor Source Code
#include <stdlib.h>
#include <unistd.h>
#include <string.h>
#include <string>
#include <fcntl.h>
#include <assert.h>
#include <sys/poll.h>
#include <thread>
#include <mutex>
#include <zmq.h>
#include <fstream>
#include <iostream>
std::mutex mutex;
void *publisher = 0; /* Publishing socket */
int SW1 = 0; /* Switch status */
int LED = 0; /* LED status */
int stop = 0; /* Non-zero when shutting down */
int gp_SW1 = 22; /* GPIO 22 (input) */
int gp_LED = 27; /* GPIO 22 (output) */
int fd_SW1 = -1; /* Open fd for SW1 */

## Slide 13
Sensor Source Code
void publish_LED(void)
{
std::string msg = "led:" + std::to_string(LED);
{
int rc;
std::lock_guard<std::mutex> gaurd(mutex);
rc = zmq_send(publisher, msg.c_str(), 5, 0);
assert(rc != -1);
}
}
void publish_SW1(void)
{
std::string msg = "sw1:" + std::to_string(SW1);
{
int rc;
std::lock_guard<std::mutex> gaurd(mutex);
rc = zmq_send(publisher, msg.c_str(), 5, 0);
assert(rc != -1);
}
}

## Slide 14
Sensor Source Code
typedef enum
{
gp_export = 0, /* /sys/class/gpio/export */
gp_unexport, /* /sys/class/gpio/unexport */
gp_direction, /* /sys/class/gpio%d/direction */
gp_edge, /* /sys/class/gpio%d/edge */
gp_value /* /sys/class/gpio%d/value */
}
gpio_path_t;
std::string gpio_getpath(int pin, gpio_path_t type)
{
std::string paths[] =
{
"export", "unexport", "gpio" + std::to_string(pin) + "/direction", "gpio" + std::to_string(pin) + "/edge",
"gpio" + std::to_string(pin) + "/value"
};
return "/sys/class/gpio/" + paths[type];
}

## Slide 15
Sensor Source Code
int gpio_open_edge(int pin, std::string edge)
{
std::string address;
std::fstream f;
address = gpio_getpath(pin, gp_export);
f.open(address, std::ios::out);
f << pin << std::endl;
f.close();
address = gpio_getpath(pin, gp_direction);
f.open(address, std::ios::out);
f << "in" << std::endl;
f.close();
address = gpio_getpath(pin, gp_edge);
f.open(address, std::ios::out);
f << edge << std::endl;
f.close();
address = gpio_getpath(pin, gp_value);
int fd;
fd = open(address.c_str(), O_RDWR);
return fd;
}

## Slide 16
Sensor Source Code
int gpio_open_output(int pin)
{
std::string address;
std::fstream f;
address = gpio_getpath(pin, gp_export);
f.open(address, std::ios::out);
f << pin << std::endl;
f.close();
address = gpio_getpath(pin, gp_direction);
f.open(address, std::ios::out);
f << "out" << std::endl; f.close();
address = gpio_getpath(pin, gp_value);
int fd;
fd = open(address.c_str(), O_WRONLY);
return fd;
}

## Slide 17
Sensor Source Code
void gpio_close(int pin)
{
std::string address;
std::fstream f;
address = gpio_getpath(pin, gp_unexport);
f.open(address, std::ios::out);
f << pin << std::endl;
f.close();
}
void gpio_write(int fd, int dbit)
{
write(fd, dbit ? "1\n" : "0\n", 2);
}
void SW1_monitor_thread()
{
while (!stop)
{
auto rc = gpio_poll(fd_SW1);
SW1 = rc;
publish_SW1();
}
}

## Slide 18
Sensor Source Code
int gpio_poll(int fd)
{
struct pollfd polls;
polls.fd = fd; /* /sys/class/gpio17/value */
polls.events = POLLPRI; /* Exceptions */
int rc;
do
{
rc = poll(&polls, 1, -1); /* Block */
}
while (rc < 0 && errno == EINTR);
assert(rc > 0);
lseek(fd, 0, SEEK_SET);
char buf[32];
auto n = read(fd, buf, sizeof buf);
assert(n>0);
buf[n] = 0;
rc = std::sscanf(buf, "%d", &n);
assert(rc == 1);
return n; /* Return value */
}

## Slide 19
Sensor Source Code
void console_thread()
{
while (!stop)
{
sleep(3);
publish_SW1();
publish_LED();
}
}
int main(int argc, char **argv)
{
int fd_LED = -1; /* GPIO 27 */
fd_LED = gpio_open_output(gp_LED);
if (fd_LED < 0)
{
std::cout << strerror(errno) << ": Opening GPIO " << gp_LED << " for output.\n"; return 1;
} /* Open GPIO for SW1 */

## Slide 20
Sensor Source Code
fd_SW1 = gpio_open_edge(22, "both");
if (fd_SW1 < 0)
{
std::cout << strerror(errno) << ": Opening GPIO " << gp_SW1 << " for input.\n";
return 1;
}
auto context = zmq_ctx_new();
assert(context);
publisher = zmq_socket(context, ZMQ_PUB);
assert(publisher);
std::string service_sensor_pub = "tcp://*:9999";
int rc = 0;
rc = zmq_bind(publisher, service_sensor_pub.c_str());
assert(!rc);
auto console = zmq_socket(context, ZMQ_PULL);
assert(console);

## Slide 21
Sensor Source Code
std::string service_sensor_pull = "tcp://*:9998";
rc = zmq_bind(console, service_sensor_pull.c_str());
assert(rc != -1);
SW1 = 0;
publish_SW1();
publish_LED();
std::thread thread1(SW1_monitor_thread);
std::thread thread2(console_thread);

## Slide 22
Sensor Source Code
while(true)
{
char buf[256];
rc = zmq_recv(console, buf, sizeof buf - 1, 0);
if (rc > 0)
{
buf[rc] = 0;
std::string getCmd = buf;
if(getCmd.substr(0, 4) == "led:")
{
buf[rc] = 0;
LED = std::stoi(getCmd.substr(4, 5)); gpio_write(fd_LED, LED);
publish_LED();
}
if(getCmd.substr(0, 5) == "stop:")
{
stop = 1;
break;
}
}
}

## Slide 23
Sensor Source Code
std::lock_guard<std::mutex> gaurd(mutex);
zmq_close(console);
console = 0;
rc = zmq_send(publisher, "off:", 4, 0);
assert(rc != -1);
sleep(3);
zmq_close(publisher);
publisher = 0;
gpio_close(gp_SW1);
gpio_close(gp_LED);
return 0;
}

## Slide 24
Console Source Code
The console program is an ncurses-based program. It provides the user with a full-screen display without the complexity of programming a GUI program (an exercise left to the interested reader).
The main program initiates curses mode in lines 204 through 207. Prior to that, the ØMQ library is used to subscribe to the sensor’s published data in lines 184 through 196. Notice that when subscribing, you must indicate what subscriptions you want. Not setting any ZMQ_SUBSCRIBE options will result in no messages being received.
Lines 198 to 202 initiate a push connection to the sensor, so commands may be delivered from the console to the sensor. Note that all running consoles will also establish this connection. Any console can control the sensor.
The main console loop from lines 226 through 243 receives the subscribed messages and displays them on the console. That’s all it does.
The command_center thread is shown in lines 112 to 161. It simply reads a keystroke in line 125 and then dispatches the command in line 132. The ncurses library is not thread safe, so mutex locking is used to prevent more than one thread from attempting to use that library simultaneously.

## Slide 25
Console Source Code
#include <string.h>
#include <assert.h>
#include "pdcourse\curses.h“
#include <string>
#include <zmq.h>
#include <thread>
#include <mutex>
#include <iostream>
std::mutex mutex;
struct DeviceStatus
{
int SW1 = -1; /* Known status of SW1 */
int LED = -1; /* Known status of LED */
};

## Slide 26
Console Source Code
void post_SW1(DeviceStatus devState)
{
std::lock_guard<std::mutex> gaurd(mutex);
attrset(A_REVERSE);
mvprintw(3, 4, "SW1:");
attrset(A_NORMAL);
move(3, 9);
if (devState.SW1 < 0)
addstr("???");
else
{
if (devState.SW1)
{
attrset(A_BOLD); /* Blink when switch on */
addstr("On ");
}
else
{
attrset(A_NORMAL);
addstr("Off"); /* SW1 is off */
}
}

## Slide 27
Console Source Code
attrset(A_NORMAL);
if (devState.SW1 >= 0 || devState.LED >= 0)
mvprintw(7, 15, "ONLINE ");
move(7, 12);
refresh();
}
void post_LED(DeviceStatus devState)
{
std::lock_guard<std::mutex> gaurd(mutex);
attrset(A_REVERSE);
mvprintw(5, 4, "LED:");
attrset(A_NORMAL);
move(5, 9);

## Slide 28
Console Source Code
if (devState.LED < 0)
addstr("???");
else
{
if (devState.LED)
{
attrset(A_BOLD);
addstr("On "); /* LED is now on */
}
else
{
attrset(A_NORMAL);
addstr("Off"); /* LED is now off */
}
}
attrset(A_NORMAL);
if (devState.SW1 >= 0 || devState.LED >= 0)
mvprintw(7, 15, "ONLINE ");
move(7, 12);
refresh();
}

## Slide 29
Console Source Code
void post_offline(DeviceStatus & devState)
{
devState.SW1 = -1;
devState.LED = -1;
{
std::lock_guard<std::mutex> gaurd(mutex);
attrset(A_REVERSE | A_BLINK);
mvprintw(7, 15, "OFFLINE");
refresh();
}
post_LED(devState);
post_SW1(devState);
}

## Slide 30
Console Source Code
void command_center(void * console)
{
int rc;
while(1)
{
{
std::lock_guard<std::mutex> gaurd(mutex);
move(7, 12); /* Move cursor to command point */ refresh();
}
rc = std::getchar();
{
std::lock_guard<std::mutex> gaurd(mutex);
mvaddch(7, 12, rc); /* Echo character that was typed */ refresh();
}

## Slide 31
Console Source Code
    switch (rc)
    {
    case '0': /* Tell sensor to turn off LED */ rc = zmq_send(console, "led:0", 5, 0);
    assert(rc != -1);
    break;
    case '1': /* Tell sensor to turn on LED */
    rc = zmq_send(console, "led:1", 5, 0);
    assert(rc != -1);
    break;
    case 'x’:
    case 'X':
    rc = zmq_send(console, "stop:", 5, 0);
    assert(rc != -1);
    break;
    case 'q’:
    case 'Q': /* Quit the command console */
    Sleep(1);
    clear();
    refresh();
endwin();
exit(0);
break;
}
}
}

## Slide 32
Console Source Code
void main(int argc, char **argv)
{
std::string host_name("localhost"); /* Default host name */
if (argc > 1)
host_name = argv[1];
auto context = zmq_ctx_new();
assert(context);
auto subscriber = zmq_socket(context, ZMQ_SUB);
assert(subscriber);
int rc;
std::string service_sensor_pub = "tcp://" + host_name + ":9999";
rc = zmq_connect(subscriber, service_sensor_pub.c_str());
if (rc == -1)
std::cerr << "zmq_connect\n";
rc = zmq_setsockopt(subscriber, ZMQ_SUBSCRIBE, "sw1:", 4);
assert(rc != -1);
rc = zmq_setsockopt(subscriber, ZMQ_SUBSCRIBE, "led:", 4);
assert(rc != -1);
rc = zmq_setsockopt(subscriber, ZMQ_SUBSCRIBE, "off:", 4);
assert(rc != -1);

## Slide 33
Console Source Code
auto console = zmq_socket(context, ZMQ_PUSH);
assert(console);
std::string service_sensor_pull = "tcp://" + host_name + ":9998";
rc = zmq_connect(console, service_sensor_pull.c_str());
assert(!rc);
initscr();
cbreak();
noecho();
nonl();
clear();
box(stdscr, '|', '-’);
move(1, 2);
printw("Receiving sensor at: %s", service_sensor_pub.c_str());
attrset(A_BLINK);
mvaddstr(7, 2, "Commands:");
attrset(A_NORMAL);
mvaddstr(9, 2, "0 - Turn remote LED off.");
mvaddstr(10, 2, "1 - Turn remote LED on.");
mvaddstr(11, 2, "X - Shutdown sensor node.");
mvaddstr(12, 2, "Q - Quit the console.");
mvprintw(7, 15, "Online?");

## Slide 34
Console Source Code
DeviceStatus devState;
post_LED(devState);
post_SW1(devState);
std::thread thread(command_center, console);
assert(!rc);
while(1)
{
char buf[1024];
rc = zmq_recv(subscriber, buf, sizeof buf - 1, 0);
assert(rc >= 0 && rc < sizeof buf - 1);
buf[rc] = 0;
auto bufStr = std::string(buf);
if (bufStr.substr(0, 4) == "off:")
post_offline(devState);
else if (bufStr.substr(0, 4) == "sw1:")
{
devState.SW1 = std::stoi(bufStr.substr(4, 5));
post_SW1(devState);
}
else if (bufStr.substr(0, 4) == "led:")
{
devState.LED = std::stoi(bufStr.substr(4, 5)); post_LED(devState);
}
}
}

## Slide 35
Contact us
www.e-system.ir
Info@e-system.ir