## Slide 1
Leap Motion
workshop
Lecturer : Reza Arjmandi

## Slide 2
Leap Motion, Inc. is an American company that manufactures and markets a computer hardware sensor device that supports hand and finger motions as input, analogous to a mouse, but requires no hand contact or touching.
In 2016, the company released new software designed for hand tracking in virtual reality.
Introduction

## Slide 3
The Leap Motion controller is a small USB peripheral device which is designed to be placed on a physical desktop, facing upward. It can also be mounted onto a virtual reality headset.
Application

## Slide 4
Using two monochromatic IR cameras and three infrared LEDs, the device observes a roughly hemispherical area, to a distance of about 1 meter.
The LEDs generate pattern-less IR light and the cameras generate almost 200 frames per second of reflected data.
This is then sent through a USB cable to the host computer, where it is analyzed by the Leap Motion software using "complex maths" in a way that has not been disclosed by the company, in some way synthesizing 3D position data by comparing the 2D frames generated by the two cameras.
The smaller observation area and higher resolution of the device differentiates the product from the Kinect, which is more suitable for whole-body tracking in a space the size of a living room.
In a demonstration to CNET, the controller was shown to perform tasks such as navigating a website, using pinch-to-zoom gestures on maps, high-precision drawing, and manipulating complex 3D data visualizations.
Technology

## Slide 5
V2 Tracking
Software SDK
Orion
Unity Assetes

## Slide 6
V2 Tracking

## Slide 7
Leap Motion App Home

## Slide 8
LeapSDK

## Slide 9
Leap Motion SDK

## Slide 10
Coordinate System

## Slide 11
Leap Motion Simple Example

## Slide 12
C++ SDK
#include "Leap.h“
#include <iostream>
using namespace Leap;
class SampleListener : public Listener
{
public:
virtual void onInit(const Controller&);
virtual void onConnect(const Controller&);
virtual void onDisconnect(const Controller&);
virtual void onExit(const Controller&);
virtual void onFrame(const Controller&);
virtual void onFocusGained(const Controller&);
virtual void onFocusLost(const Controller&);
virtual void onDeviceChange(const Controller&);
virtual void onServiceConnect(const Controller&);
virtual void onServiceDisconnect(const Controller&);
};
Example 1

## Slide 13
C++ SDK
void main(int argc, char** argv)
{
SampleListener listener;
Controller controller
controller.addListener(listener);
std::cout << "Press Enter to quit..." << std::endl;
std::cin.get();
controller.removeListener(listener);
}
Example 1

## Slide 14
C++ SDK
void SampleListener::onInit(const Controller& controller)
{
std::cout << "Initialized" << std::endl;
}
void SampleListener::onConnect(const Controller& controller)
{
std::cout << "Connected" << std::endl;
controller.enableGesture(Gesture::TYPE_CIRCLE);
controller.enableGesture(Gesture::TYPE_KEY_TAP);
controller.enableGesture(Gesture::TYPE_SCREEN_TAP);
controller.enableGesture(Gesture::TYPE_SWIPE);
}
void SampleListener::onDisconnect(const Controller& controller)
{
std::cout << "Disconnected" << std::endl;
}
Example 1

## Slide 15
C++ SDK
void SampleListener::onExit(const Controller& controller)
{
std::cout << "Exited" << std::endl;
}
void SampleListener::onFrame(const Controller& controller)
{
auto frame = controller.frame();
std::cout << "Frame id: " << frame.id()
<< ", timestamp: " << frame.timestamp()
<< ", hands: " << frame.hands().count()
<< ", extended fingers: " <<
frame.fingers().extended().count()
<< ", tools: " << frame.tools().count()
<< ", gestures: " << frame.gestures().count() << std::endl;
}
Example 1

## Slide 16
C++ SDK
void SampleListener::onFocusGained(const Controller& controller)
{
std::cout << "Focus Gained" << std::endl;
}
void SampleListener::onFocusLost(const Controller& controller)
{
std::cout << "Focus Lost" << std::endl;
}
void SampleListener::onServiceConnect(const Controller& controller)
{
std::cout << "Service Connected" << std::endl;
}
void SampleListener::onServiceDisconnect(const Controller& controller)
{
std::cout << "Service Disconnected" << std::endl;
}
Example 1

## Slide 17
C++ SDK
void SampleListener::onDeviceChange(const Controller& controller)
{
std::cout << "Device Changed" << std::endl;
auto devices = controller.devices();
for (const auto& device : devices)
{
std::cout << "id: " << devices[i].toString() << std::endl;
std::cout << " isStreaming: " << (devices[i].isStreaming() ? "true" : "false") << std::endl;
}
}
Example 1

## Slide 18
Introduction ZMQ Library

## Slide 19
Data Stream Network

## Slide 20
C++ SDK
auto context = zmq_ctx_new();
auto publisher = zmq_socket(context, ZMQ_PUB);
zmq_bind(publisher, "tcp://*:9999");
zmq_send(publisher, BroadcastMSG.c_str(), BroadcastMSG.length(), 0);
ZMQ - Publisher

## Slide 21
C++ SDK
auto context = zmq_ctx_new();
auto console = zmq_socket(context, ZMQ_SUB);
zmq_connect(console, service_sensor_sub.c_str());
zmq_setsockopt(console, ZMQ_SUBSCRIBE, "HL:", 3);
char buf[256];
zmq_recv(console, buf, sizeof buf - 1, 0);
ZMQ - Subscriber

## Slide 22
Controling DC Motor Project

## Slide 23
Windows Side Project

## Slide 24
C++ SDK
#include "Leap.h"
#include <string>
#include <iostream>
#include <zmq.h>
using namespace Leap;
std::string BroadcastMSG = "None";
Controling DC Motor Project

## Slide 25
C++ SDK
class SampleListener : public Listener
{
public:
virtual void onFrame(const Controller& controller)
{
const auto frame = controller.frame();
auto hands = frame.hands();
auto normPalmPos = hands[0].palmNormal();
auto palmPos = hands[0].palmPosition();
if (hands[0].isValid())
{
int pwm = palmPos.y / 6.5;
if (pwm >= 100)
pwm = 99;
BroadcastMSG = normPalmPos.x > 0 ? "CW:" + std::to_string(pwm) : "CC:" + std::to_string(pwm);
}
}
};
Controling DC Motor Project

## Slide 26
C++ SDK
void main()
{
SampleListener listener;
Controller controller;
controller.addListener(listener);
auto context = zmq_ctx_new(); auto publisher = zmq_socket(context, ZMQ_PUB);
zmq_bind(publisher, "tcp://*:9999");
long long int counter = 0;
while (true)
{
if (BroadcastMSG != "None")
{
zmq_send(publisher, BroadcastMSG.c_str(), 5, 0);
std::cout << "Broadcast Message " << counter++ << " : " << BroadcastMSG << std::endl;
BroadcastMSG = "None";
}
}
controller.removeListener(listener);
}
Controling DC Motor Project

## Slide 27
Raspberry Pi Side Project

## Slide 28
Project Schematic

## Slide 29
L298 Schematic

## Slide 30
L298 Schematic

## Slide 31
C++ SDK
#include <wiringPi.h>
#include <softPwm.h>
#include <string>
#include <assert.h>
#include <thread>
#include <zmq.h>
#include <iostream>
enum {CW = 1, CCW = 2} Direction;
int Speed = 0;
int EnablePin = 18;
int In1Pin = 23;
int In2Pin = 24;
Controling DC Motor Project

## Slide 32
C++ SDK
void CW_Rotate()
{
digitalWrite(In1Pin, LOW);
digitalWrite(In2Pin, HIGH);
}
void CCW_Rotate()
{
digitalWrite(In1Pin, HIGH);
digitalWrite(In2Pin, LOW);
}
Controling DC Motor Project

## Slide 33
C++ SDK
void MotorAction()
{
softPwmCreate(EnablePin, 0, 100);
pinMode(In1Pin, OUTPUT);
pinMode(In2Pin, OUTPUT);
CW_Rotate();
while (1)
{
if (Direction == CW)
CW_Rotate();
else
CCW_Rotate();
softPwmWrite(EnablePin, Speed);
}
}
Controling DC Motor Project

## Slide 34
C++ SDK
int main(void)
{
wiringPiSetupSys();
std::thread t(MotorAction);
auto context = zmq_ctx_new();
assert(context);
auto console = zmq_socket(context, ZMQ_SUB);
assert(console);
std::string service_sensor_sub = "tcp://192.168.43.87:9999";
auto rc = zmq_connect(console, service_sensor_sub.c_str());
assert(rc != -1);
zmq_setsockopt(console, ZMQ_SUBSCRIBE, "CW:", 3);
zmq_setsockopt(console, ZMQ_SUBSCRIBE, "CC:", 3);
Controling DC Motor Project

## Slide 35
C++ SDK
while (true)
{
char buf[256];
rc = zmq_recv(console, buf, sizeof buf - 1, 0);
if (rc > 0)
{
buf[rc] = 0;
std::string getCmd = buf;
Direction = getCmd.substr(0, 3) == "CW:" ? CW : CCW;
auto getPwm = std::stoi(getCmd.substr(3, 5));
getPwm *= 2;
getPwm = getPwm > 99 ? 99 : getPwm;
Speed = getPwm;
std::cout << getCmd <<std::endl;
}
}
return 0;
}
Controling DC Motor Project

## Slide 36
Controlling 3D Volume Project

## Slide 37
C++ SDK
#include <vtkCubeSource.h>
#include <vtkSmartPointer.h>
#include <vtkPolyDataMapper.h>
#include <vtkActor.h>
#include <vtkRenderWindow.h>
#include <vtkRenderer.h>
#include <vtkRenderWindowInteractor.h>
#include <vtkCamera.h>
#include "Leap.h"
using namespace Leap;
Vector origin;
Vector move;
Vector center;
Vector originVector;
Vector rotateVec;
bool freez = false;
Controlling 3D Volume Project

## Slide 38
C++ SDK
vtkSmartPointer<vtkRenderWindowInteractor> renderWindowInteractor;
vtkSmartPointer<vtkCamera> camera;
vtkSmartPointer<vtkActor> actor;
class SampleListener : public Listener
{
public:
virtual void onFrame(const Controller& controller)
{
const auto frame = controller.frame();
const auto hand1 = frame.hands()[0];
const auto hand2 = frame.hands()[1];
Controlling 3D Volume Project

## Slide 39
C++ SDK
if (hand1.isValid())
{
if (hand2.isValid())
freez = true;
else
freez = false;
rotateVec = hand1.palmNormal();
center = hand1.palmPosition();
}
}
};
Controlling 3D Volume Project

## Slide 40
C++ SDK
class vtkTimerCallback : public vtkCommand
{
public:
static vtkTimerCallback *New()
{
auto cb = new vtkTimerCallback;
return cb;
}
virtual void Execute(vtkObject * caller, unsigned long eventId, void *vtkNotUsed(callData))
{
auto interactor = vtkRenderWindowInteractor::SafeDownCast(caller);
if (!freez)
{
actor->RotateX((rotateVec.x - originVector.x) * 200);
actor->RotateY((rotateVec.y - originVector.y) * 200);
actor->RotateX((rotateVec.z - originVector.z) * 200);
Controlling 3D Volume Project

## Slide 41
C++ SDK
double x, y, z;
camera->GetPosition(x, y, z);
camera->SetPosition(x, y, center.y * 2);
}
interactor->Render();
}
};
Controlling 3D Volume Project

## Slide 42
C++ SDK
void main(int argc, char *argv[])
{
originVector.x = 0.0;
originVector.y = 0.0;
originVector.z = -1.0;
rotateVec.x = 0.0;
rotateVec.y = 0.0;
rotateVec.z = -1.0;
SampleListener listener;
Controller controller;
controller.addListener(listener);
auto cubeSource = vtkSmartPointer<vtkCubeSource>::New();
cubeSource->SetCenter(0.0, 0.0, 0.0);
cubeSource->SetXLength(100.0);
cubeSource->SetYLength(100.0);
cubeSource->SetZLength(100.0);
Controlling 3D Volume Project

## Slide 43
C++ SDK
auto mapper = vtkSmartPointer<vtkPolyDataMapper>::New();
mapper->SetInputConnection(cubeSource->GetOutputPort());
actor = vtkSmartPointer<vtkActor>::New();
actor->SetMapper(mapper);
auto renderer = vtkSmartPointer<vtkRenderer>::New();
renderer->AddActor(actor);
renderer->SetBackground(.1, .3, .2); // Background color dark green
camera = vtkSmartPointer<vtkCamera>::New();
renderer->SetActiveCamera(camera);
renderer->ResetCamera();
camera->SetClippingRange(1, 5000);
auto renderWindow = vtkSmartPointer<vtkRenderWindow>::New();
renderWindow->AddRenderer(renderer);
renderWindow->SetWindowName(argv[0]);
renderWindow->SetSize(1000, 1000);
Controlling 3D Volume Project

## Slide 44
C++ SDK
renderWindowInteractor = vtkSmartPointer<vtkRenderWindowInteractor>::New();
renderWindowInteractor->SetRenderWindow(renderWindow);
renderWindowInteractor->SetInteractorStyle(nullptr);
renderWindowInteractor->Initialize();
auto callback = vtkSmartPointer<vtkTimerCallback>::New();
renderWindowInteractor->AddObserver(vtkCommand::TimerEvent, callback);
renderWindowInteractor->CreateRepeatingTimer(10);
renderWindow->Render();
renderWindowInteractor->Start();
controller.removeListener(listener);
}
Controlling 3D Volume Project

## Slide 46
Unity 3D Game Engine

## Slide 47
Vuforia Augmented Reality Platform

## Slide 48
Controlling LED Array Project

## Slide 49
Windows Side Project

## Slide 50
Leap Motion Gestures

## Slide 51
C++ SDK
#include "Leap.h"
#include <string>
#include <iostream>
#include <zmq.h>
using namespace Leap;
std::string BroadcastMSG = "None";
Controling LED Array Project

## Slide 52
C++ SDK
class SampleListener : public Listener
{
public:
virtual void onFrame(const Controller& controller)
{
const auto frame = controller.frame();
auto hands = frame.hands();
if (hands[0].isValid() && hands[1].isValid())
{
BroadcastMSG = "HR:HL";
return;
}
Controling LED Array Project

## Slide 53
C++ SDK
auto gestures = frame.gestures();
for (const auto &gesture : gestures)
{
if (gesture.isValid())
{
switch (gesture.type())
{
case Gesture::Type::TYPE_SWIPE:
SetBroadcastMsg(frame.hands(), "HR:TYPE_SWIPE", "HL:TYPE_SWIPE");
break;
case Gesture::Type::TYPE_KEY_TAP:
SetBroadcastMsg(frame.hands(), "HR:TYPE_KEY_TAP", "HL:TYPE_KEY_TAP");
break;
case Gesture::Type::TYPE_SCREEN_TAP:
SetBroadcastMsg(frame.hands(), "HR:TYPE_SCREEN_TAP", "HL:TYPE_SCREEN_TAP");
break;
Controling LED Array Project

## Slide 54
C++ SDK
case Gesture::Type::TYPE_CIRCLE:
SetBroadcastMsg(frame.hands(), "HR:TYPE_CIRCLE", "HL:TYPE_CIRCLE");
break;
}
}
}
}
Controling LED Array Project

## Slide 55
C++ SDK
private:
void SetBroadcastMsg(const Leap::HandList& hands ,const std::string& msgR, const std::string& msgL)
{
if (hands[0].isValid())
{
if (hands[0].isRight())
{
BroadcastMSG = msgR;
return;
}
else
{
BroadcastMSG = msgL;
return;
}
}
Controling LED Array Project

## Slide 56
C++ SDK
if (hands[1].isValid())
{
if (hands[1].isRight())
{
BroadcastMSG = msgR;
return;
}
else
{
BroadcastMSG = msgL;
return;
}
}
}
};
Controling LED Array Project

## Slide 57
C++ SDK
int main()
{
SampleListener listener;
Controller controller;
controller.enableGesture(Leap::Gesture::TYPE_KEY_TAP, true);
controller.enableGesture(Leap::Gesture::TYPE_CIRCLE, true);
controller.enableGesture(Leap::Gesture::TYPE_SCREEN_TAP, true);
controller.enableGesture(Leap::Gesture::TYPE_SWIPE, true);
controller.addListener(listener);
auto context = zmq_ctx_new();
auto publisher = zmq_socket(context, ZMQ_PUB);
zmq_bind(publisher, "tcp://*:9999");
Controling LED Array Project

## Slide 58
C++ SDK
long long int counter = 0;
while (true)
{
if (BroadcastMSG != "None")
{
zmq_send(publisher, BroadcastMSG.c_str(), BroadcastMSG.length(), 0);
std::cout << "Broadcast Message " << counter++ << " : " << BroadcastMSG << std::endl;
Sleep(500);
BroadcastMSG = "None";
}
}
controller.removeListener(listener);
return 0;
}
Controling LED Array Project

## Slide 59
Raspberry Pi Side Project

## Slide 60
C++ SDK
#include <wiringPi.h>
#include <string>
#include <assert.h>
#include <thread>
#include <zmq.h>
#include <iostream>
enum Hand {Right = 1, Left = 2};
enum {Static = 1, Blink = 2, CircleR = 3, CircleL = 4, BlinkAll = 5 } Mode;
int LEDList[9] = { 2, 3, 4, 17, 27, 22, 23, 24, 8 };
int LEDPos;
Controling LED Array Project

## Slide 61
C++ SDK
void NextLEDL()
{
LEDPos++;
if (LEDPos > 8)
LEDPos = 0;
}
void NextLEDR()
{
LEDPos--;
if (LEDPos < 0)
LEDPos = 8;
}
Controling LED Array Project

## Slide 62
C++ SDK
void ResetGPIO()
{
for (const auto &led : LEDList)
{
pinMode(led, OUTPUT);
digitalWrite(led, LOW);
}
}
void LEDAction()
{
int blinkValue = 1;
while (1)
{
ResetGPIO();
switch (Mode)
{
Controling LED Array Project

## Slide 63
C++ SDK
case Static:
{
pinMode(LEDList[LEDPos], OUTPUT);
digitalWrite(LEDList[LEDPos], HIGH);
break;
}
case Blink:
{
pinMode(LEDList[LEDPos], OUTPUT);
digitalWrite(LEDList[LEDPos], blinkValue);
blinkValue = !blinkValue;
delay(500);
break;
}
Controling LED Array Project

## Slide 64
C++ SDK
case CircleR:
{
pinMode(LEDList[LEDPos], OUTPUT);
digitalWrite(LEDList[LEDPos], HIGH);
NextLEDR();
delay(200);
break;
}
case CircleL:
{
pinMode(LEDList[LEDPos], OUTPUT);
digitalWrite(LEDList[LEDPos], HIGH);
NextLEDL();
delay(200);
break;
}
Controling LED Array Project

## Slide 65
C++ SDK
case BlinkAll:
{
for (const auto & led : LEDList)
{
pinMode(led, OUTPUT);
digitalWrite(led, blinkValue);
}
blinkValue = !blinkValue;
delay(500);
break;
}
}
}
}
Controling LED Array Project

## Slide 66
C++ SDK
int main(void)
{
wiringPiSetupSys();
Mode = Static;
LEDPos = 0;
std::thread t(LEDAction);
auto context = zmq_ctx_new();
assert(context);
auto console = zmq_socket(context, ZMQ_SUB);
assert(console);
std::string service_sensor_sub = "tcp://192.168.43.87:9999";
Controling LED Array Project

## Slide 67
C++ SDK
auto rc = zmq_connect(console, service_sensor_sub.c_str());
assert(rc != -1);
zmq_setsockopt(console, ZMQ_SUBSCRIBE, "HL:", 3);
zmq_setsockopt(console, ZMQ_SUBSCRIBE, "HR:", 3);
while (true)
{
char buf[256];
rc = zmq_recv(console, buf, sizeof buf - 1, 0);
if (rc > 0)
{
buf[rc] = 0;
std::string getCmd = buf;
auto hand = getCmd.substr(0, 3) == "HR:" ? Right : Left;
if (getCmd.substr(3, 5) == "HL")
{
Mode = BlinkAll;
std::cout << getCmd << std::endl;
}
Controling LED Array Project

## Slide 68
C++ SDK
if (getCmd.substr(3, 13) == "TYPE_SWIPE")
{
hand == Right ? NextLEDL() : NextLEDR();
std::cout << getCmd << std::endl;
}
else if (getCmd.substr(3, 14) == "TYPE_CIRCLE") {
Mode = hand == Right ? CircleR :CircleL;
std::cout << getCmd << std::endl;
}
else if (getCmd.substr(3, 15) == "TYPE_KEY_TAP")
{
Mode = Blink;
std::cout << getCmd << std::endl;
}
else if (getCmd.substr(3, 18) == "TYPE_SCREEN_TAP")
{
Mode = Static;
std::cout << getCmd << std::endl;
}}}
return 0;
}
Controling LED Array Project