## Slide 1: Internet Of things
Lecturer: Reza Arjmandi
Summer 2016
Preface:
In this chapter, you will learn how your Raspberry Pi can participate in the Internet of Things in various ways.

## Slide 2
Measuring the Raspberry Pi CPU Temperature
You want to know just how hot your Raspberry Pi’s CPU is getting.
Use the os library to access the temperature sensor built into the Broadcom chip.
  import os, time
  while True:
    dev = os.popen('/opt/vc/bin/vcgencmd measure_temp')
    cpu_temp = dev.read()
    print(cpu_temp)
    time.sleep(1)
    When you run this program, it will report the temperature. Note that the message printed is actually a string with temp= before the temperature and 'C after it.
    $ python cpu_temp.py
    temp=33.6'C
    temp=33.6'C

## Slide 3
Measuring the Raspberry Pi CPU Temperature
If you want the temperature as a number rather than a string, you need to chop off the extra text and then convert the number to a float.
import os, time
while True:
  dev = os.popen('/opt/vc/bin/vcgencmd measure_temp')
  cpu_temp_s = dev.read()[5:-3] # top and tail string
  cpu_temp = float(cpu_temp_s)
  print(cpu_temp)
  time.sleep(1)

## Slide 4
Displaying Sensor Readings on a Web Page
You want to display sensor readings from your Raspberry Pi on a web page that automatically updates.
Use the bottle web server and some fancy JavaScript to automatically update your display.

## Slide 5
Displaying Sensor Readings on a Web Page
  There are four files for this example, which are contained in the folder web_sensor:
  web_sensor.py
    Contains the Python code for the bottle server
    main.html
    Contains the web page that will be displayed in your browser
    justgage.1.0.1.min.js
    A third-party JavaScript library that displays the temperature meter
    raphael.2.1.0.min.js
    A library used by the justgage library
    To run the program, change directory to web_sensor and then run the Python program using:
    $ sudo python web_sensor.py
    Then open a browser, either on the same Raspberry Pi or any computer on the same network as the Raspberry Pi, and enter the IP address of the Raspberry Pi into the browser’s address bar.

## Slide 6
WebSensor.py Project
  The main program (web_sensor.py) is actually quite concise:
  import os, time
  from bottle import route, run, template
  def CpuTemp():
  dev = os.popen('/opt/vc/bin/vcgencmd measure_temp')
  temp = dev.read()[5:-3]
  return temp
  @route('/temp')
  def Temp():
  return CpuTemp()
  @route('/')
  def index():
  return template('main.html')
  @route('/raphael')
  def index():
  return template('raphael.2.1.0.min.js')

## Slide 7
WebSensor.py Project
  @route('/justgage')
  def index():
  return template('justgage.1.0.1.min.js')
  run(host=‘0.0.0.0', port=80)
  The function CpuTemp reads the temperature of the Raspberry Pi’s CPU, as described in Previous Recipe
  Four routes are then defined for the bottle web server. The first (/temp) returns a string containing the CPU temperature in degrees C. The root route (/) returns the main HTML template for the page (main.html). The other two routes provide access to copies of the raphael and justgage JavaScript libraries.

## Slide 8
main.html File
  The file main.html mostly contains the JavaScript to render the user interface.
  <html>
  <head>
  <script src="http://ajax.googleapis.com/ajax/libs/jquery/1.7.2/jquery.min.js" type="text/javascript" charset="utf-8"></script>
  <script src="raphael"></script>
  <script src="justgage"></script>
  <script>
  function callback(tempStr, status)
  {
  if (status == "success")
  {
  temp = parseFloat(tempStr).toFixed(2);
  g.refresh(temp);
  setTimeout(getReading, 1000);
  }

## Slide 9
main.html File
  else
  {
  alert("There was a problem");
  }
  }
  function getReading()
  {
  $.get('/temp', callback);
  }
  </script>
  </head>
  <body>
  <div id="gauge" class="200x160px"></div>
  <script>
  var g = new JustGage({id: "gauge", value: 0, min: 10, max: 60,title: "CPU Temp 'C" })
  getReading();
  </script>
  </body>
  </html>

## Slide 10
Displaying Sensor Readings on a Web Page
  The JQuery, Raphael, and JustGage libraries are all imported (JQuery from https:// developers.google.com/speed/libraries/#jquery and the other two from local copies).
  Getting a reading from the Raspberry Pi to the browser window is a two-stage process. First, the function getReading is called. This sends a web request with the route /temp to web_sensor.py and specifies a function called callback to be run when the web request completes. The callback function is then responsible for updating the JustGage display before setting a timeout to call getReading again after a second.

## Slide 11
Sending Email and Other Notifications with IFTTT
  You want a flexible way for your Raspberrry Pi to send notifications by email, Facebook status, Twitter, or Slack.
  This recipe is illustrated with an example that sends you an email when the CPU temperature of your Raspberry Pi exceeds a threshold.
  You need to create an account with IFTTT before you can start using it, so visit www.ifttt.com and sign up.
  Click on the Create a Recipe button. This will prompt you to first enter the IF part of the recipe and later the THAT part.
  In this case, the IF THIS part (the trigger) is going to be the receipt of a web request from your Raspberry Pi, so click on THIS and then enter Maker into the search field to find the Maker channel. Select the Maker channel and when prompted to Choose a Trigger, select the option (Receive a Web Request). This will open the form shown in following figure.

## Slide 12
Sending Email and Other Notifications with IFTTT

## Slide 13
Sending Email and Other Notifications with IFTTT
  Enter the text cpu_too_hot into the Event Name field and click Create Trigger.
  This will now move you to the THAT portion of the recipe, the action , and you will need to select an action channel. Here there are many options, but for this example you will use the Email channel, so type Email into the search field and then select the Email channel. You will see several email-related channels, including Gmail. Use the email channel, even if you are sending from a Gmail account.
  Having selected the Email channel, select the action Send Me an Email, and the form shown in following figure will be displayed

## Slide 14
Sending Email and Other Notifications with IFTTT

## Slide 15
Tor

## Slide 16
Tor
  Tor is free software for enabling anonymous communication. The name is derived from an acronym for the original software project name "The Onion Router". Tor directs Internet traffic through a free, worldwide, volunteer network consisting of more than seven thousand relays to conceal a user's location and usage from anyone conducting network surveillance or traffic analysis. Using Tor makes it more difficult for Internet activity to be traced back to the user: this includes "visits to Web sites, online posts, instant messages, and other communication forms". Tor's use is intended to protect the personal privacy of users, as well as their freedom and ability to conduct confidential communication by keeping their Internet activities from being monitored.
  Install tor:
  sudo apt-get install update
  sudo apt-get install tor

## Slide 17
PySocks
  sudo pip install PySocks
SOCKS proxy client for Python 2.6 - 3.x
TCP and UDP both supported
HTTP proxy client included but not supported or recommended (you should use urllib2's or requests' own HTTP proxy interface)
urllib2 handler included
Install PySocks:

## Slide 18
EmailIfttt.py Project
  The Python program to send the web request:
  import time,os
  MaxTemp = 37.0
  EventName = 'cpu_hot'
  BaseUrl = 'https://maker.ifttt.com/trigger/{}/with/key/{}'
  Key = 'cxotxZpzCKtUnd3m7tkIk4'
  def SendNotification(temp):
  json = "'" + '{"value1" : "' + str(temp) + '"}' + "'"
  completeUrl = BaseUrl.format(EventName, Key)
  cmd = 'curl --socks5-hostname localhost:9050 -H "Content-Type:
  application/json" -X POST -d {} {}'.format(json, completeUrl)
  os.popen(cmd)
  def CpuTemp():
  dev = os.popen('/opt/vc/bin/vcgencmd measure_temp')
  temp = dev.read()[5:-3]
  return float(temp)

## Slide 19
EmailIfttt.py Project
  while True:
  temp = CpuTemp()
  print("CPU Temp(c) : {}".format(temp))
  if temp > MaxTemp:
  print("CPU TOO Hot!")
  SendNotification(temp)
  print("No more notification for : 5")
  time.sleep(5)

## Slide 20
Sending Email and Other Notifications with IFTTT
  Before running the program, you will need to get an access key for the Maker Action channel by selecting Channels (at the top of the IFTTT web page), and then searching for Maker. Connect to the channel, and then you will see your key displayed near the bottom of the web page
  Paste the key into previous program on the line that starts KEY= and then run the program using:
  $ sudo python ifttt_cpu_temp.py
  Most of the action for this program takes place in the send_notification email. This first constructs a URL including the key and request parameter value1 (containing the temperature) and then uses the Python urllib2 to send the web request to IFTTT.
  The main loop continually checks the temperature against the MAX_TEMP, and if the CPU temperature exceeds MAX_TEMP, the web request is sent and a long sleep is started as specified by MIN_T_BETWEEN_WARNINGS to prevent your inbox from being flooded with notifications.

## Slide 21
Sending Sensor Data to ThingSpeak
  You want to log sensor data to ThingSpeak.
  Log into ThingSpeak, and from the Channels drop-down, select My Channels. Now create a new channel by completing the top of the form as shown in following Figure

## Slide 22
Sending Sensor Data to ThingSpeak
  The rest of the form can be left blank. When you have finished editing, click Save Channel at the bottom of the page. Click on the Data Import/Export tab to find a summary of the web requests that you can use, customized to the channel you just created

## Slide 23
ThingspeakData.py Project
  To send data to the channel, a web request must be sent. The Python program:
  import time, os, urllib, urllib2
  DELAY = 15
  BASEURL = 'https://api.thingspeak.com/update?api_key={}&field1={}'
  KEY = 'SNDA3NE8T2I3A5W1'
  def SendData(temp):
  completeUrl = BASEURL.format(KEY, temp)
  response = urllib2.urlopen(url=completeUrl)
  print(response.read())
  def CpuTemp():
  dev = os.popen('/opt/vc/bin/vcgencmd measure_temp')
  temperature = dev.read()[5:-3]
  return temperature

## Slide 24
Sending Sensor Data to ThingSpeak
  while True:
  temp = CpuTemp()
  print("CPU Temp (C): {}".format(temp))
  SendData(temp)
  time.sleep(DELAY)
  Run the program. On the ThingSpeak channel page on the Private View tab, you should see a graph like:

## Slide 25
Sending Email and Other Notifications with IFTTT
  The variable PERIOD is used to determine the time interval between each sending of the temperature. This period is in seconds.
  The send_data function constructs the web request, supplying the temperature in a parameter called field1.
  If your data might be of public interest—say, accurate environmental readings—then you might want to make the channel public so that anyone can make use of it. This probably isn’t the case for your Pi’s CPU temperature.

## Slide 26
Sending Tweets Using ThingSpeak
  You want to automatically send tweets from your Raspberry Pi; for example, to irritate people by telling them the temperature of your CPU.
  You could just use IFTTT and change the Action Channel to be Twitter. However, the ThingSpeak service is an alternative way of doing this.
  Start by visiting https://thingspeak.com and signing up. Then select the ThingTweet action (Following figure). You will be prompted to log in to Twitter.

## Slide 27
Sending Tweets Using ThingSpeak

## Slide 28
SendTweet.py project
  import time, os, urllib, urllib2
  MAX_TEMP = 37.0
  MIN_T_BETWEEN_WARNINGS = 60 # Minutes
  BASE_URL = 'https://api.thingspeak.com/apps/thingtweet/1/statuses/update/' KEY = '68LZC4LBMXLO6YDY’
  def send_notification(temp):
  status = 'Raspberry Pi getting hot.
  CPU temp=' + temp
  data = urllib.urlencode({'api_key' : KEY, 'status': status})
  response = urllib2.urlopen(url=BASE_URL, data=data)
  print(response.read())

## Slide 29
SendTweet.py project
  while True:
  temp = cpu_temp()
  print("CPU Temp (C): " + str(temp))
  if temp > MAX_TEMP:
  print("CPU TOO HOT!")
  send_notification(temp)
  print("No more notifications for: " + str(MIN_T_BETWEEN_WARNINGS) + " mins")
  time.sleep(MIN_T_BETWEEN_WARNINGS * 60)
  time.sleep(1)

## Slide 30
Sending Tweets Using ThingSpeak
  For full documentation of the ThingSpeak service, see https://uk.mathworks.com/help/ thingspeak/.
  You could just use IFTTT and change the Action Channel to be Twitter. However, the ThingSpeak service is an alternative way of doing this.
  Start by visiting https://thingspeak.com and signing up. Then select the ThingTweet action (Following figure). You will be prompted to log in to Twitter.

## Slide 31
Responding to Tweets Using Dweet and IFTTT
  You want your Raspberry Pi to perform some action in response to a certain hashtag or mention in a tweet.
  An efficient mechanism for monitoring tweets that does not rely on polling is to use IFTTT to spot tweets of interest and then send a web request to a service called Dweet that can push notifications to a Python program running on your Raspberry Pi (Following figure).
  For example, you could flash an LED for 10 seconds every time there is a mention of your username on Twitter by using a Raspberry Squid or an LED attached to a breadboard.

## Slide 32
Responding to Tweets Using Dweet and IFTTT

## Slide 33
Responding to Tweets Using Dweet and IFTTT
  The first step is to log in to IFTTT and then create a new recipe. Choose an action channel of New Mention of You and then click Create Trigger. For the recipe’s action channel, select Webhooks and then select the action “Make a Web Request” and complete the fields as shown in Following figure.
  The URL includes a request parameter with the ingredient of text. This will contain the body of the tweet. Although this will not be used other than to print it in the console, you might have the message displayed on an LCD screen for a more sophisticated project, so it is useful to know how to pass data from tweet to the Python program.
  Then click Create Recipe to take the IFTTT recipe live.
  The dweet.io web service operates rather like Twitter for IoT things. It has a web interface that allows you to both post and listen for dweets.

## Slide 34
Responding to Tweets Using Dweet and IFTTT

## Slide 35
Responding to Tweets Using Dweet and IFTTT
  Dweet does not require an account or any login details to make use of it; you can just have one thing (IFTTT in this case) send a message to it and have another thing (your Raspberry Pi Python program) wait for notifications from it that something you are interested in has happened. In this case, the token that links the two is tweet_about_me. This is not very unique, and if several people are trying out this example from the book at the same time, then they will get each other’s messages. To avoid this, use a more unique token (say, by adding a random string of letters and numbers to the message).
  To access Dweet from your Python program, the dweepy library needs to be installed, using the following commands:
  git clone git://github.com/paddycarey/dweepy.git
  cd dweepy
  sudo python setup.py install

## Slide 36
TwitterTrigger.py Project
  import time
  import dweepy
  import RPi.GPIO as GPIO
  KEY = 'tweet_about_me’
  OUTPUT_PIN = 18
  OUTPUT_DURATION = 10
  GPIO.setmode(GPIO.BCM)
  GPIO.setup(OUTPUT_PIN, GPIO.OUT)
  while True:
  try:
  for dweet in dweepy.listen_for_dweets_from(KEY):
  print('Tweet: ' + dweet['content']['text'])
  GPIO.output(OUTPUT_PIN, True)
  time.sleep(OUTPUT_DURATION)
  GPIO.output(OUTPUT_PIN, False)
  except Exception:
  pass

## Slide 37
Responding to Tweets Using Dweet and IFTTT
  The program uses the listen_for_dweets_from method to leave an open connection to the dweet.io server, listening for any push messages from the server as a result of a dweet arriving from IFTTT in response to a tweet. The try/except block ensure that if there is any communication outage, the program will just start the listenning process again.

## Slide 38
Contact us
www.e-system.ir
Info@e-system.ir